# MONTGOMERY COLLEGE, ROCKVILLE

# Physics, Engineering and Geosciences Department

# EE  222 – Scientific and Engineering Computation

Lab 3

Task

- Record yourself saying “I love Matlab” short phrase in about 8 seconds (leave very short pauses between the words)

  - Make sure the microphone is on.

  - In the Matlab workspace window, type

    - fs = 10000;

    - speech = wavrecord(80000,fs);

  - Hit enter and then record the sentence.

- Save the wave file as ‘your_last_name.wav’

wavwrite(speech,fs,' your_last_name.wav ');	% creates a .wav file of the signal y.

Now you have a .wav file.

- Using the mfiles provided on the web, determine the appropriate threshold and automatically label voiced, unvoiced and silence portions.

- Add white noise at 5dB SNR to your speech, and save the noisy speech as noisy_speech.wav. Repeat (3). What do you notice?

- Using the mfiles provided to obtain the spectrum of your speech in short segments.

- Manually locate at least 5 unvoiced segments that were lost in the noisy signal.

- Write a Matlab script that will automatically label voiced segments based on the spectrum. Be creative, there are several ways to do this – come up with your own.

- Research about moving average filters. Use a 10-point moving average filter to filter out the noise from noisy_speech.wav. Save the filtered speech as filtered_speech.wav. plot, listen to, observe and analyze your output.

- Repeat (3). What do you notice?

Here’s what you need to hand in:

- A report: discuss the project and the rationale behind the methods. Show plots of the noisy and clean speech and your voiced/unvoiced/silence labels. Show plots of your speech and spectra. Discuss problems 3 to 9 in detail. Show your labeled speech.

- All mfiles including your main file

- Your recorded speech file, your filtered speech file.