## Slide 1: Lecture 16: Introduction to Linear time-invariant filters; response of FIR filters to sinusoidal and exponential inputs: frequency response and system function Sections 4.2.2, 4.3, 4.4.1, 4.4.3 Sections 2.2.3, 2.3

## Slide 2
In developing the DFT, we considered discrete-time signals which are either vectors (i.e., consisted of ﬁnitely many samples) or periodic extensions thereof. We now turn our attention to general discrete-time signals, namely sequences such as
  x = x[ · ]= {x[n],n ∈ Z}
If x is a linear combination of (not necessarily periodic) sinusoids, then it also has a spectrum. Its spectrum consists of the coeﬃcients of these sinusoids given (or plotted) as a function of frequency.

## Slide 3
Linear ﬁlters can be used to alter the spectra of sequences in an immediate, “real time”, fashion. A linear ﬁlter H acts as a (linear) transformation of an input sequence x to an output sequence y. (Since the input and output spaces are inﬁnite-dimensional, this linear transformation is not represented by a ﬁnite-dimensional matrix.)
y = H(x)

## Slide 4
Analytically, the simplest discrete-time ﬁlter is the so-called ﬁnite impulse response (FIR) ﬁlter. At each sampling instant n, a new input sample is read in and stored in a buﬀer containing the M + 1 most recent input samples, i.e., x[n − M : n]. These samples are linearly combined using a ﬁxed vector b of coeﬃcients to produce an output sample y[n]. This procedure is described by a single formula:
    y[n]= b0x[n]+ b1x[n − 1] + ··· + bM x[n − M] ,n ∈ Z ,
known as the ﬁlter input-output relationship.

## Slide 5
An FIR ﬁlter has two notable properties:
  Linearity:
    If three identical ﬁlters are used on input sequences x(1), x(2) and x(3) = c1x(1) + c2x(2), then the output sequence of the third ﬁlter is the same (in terms of coeﬃcients) linear combination of the output sequences of the ﬁrst two ﬁlters, i.e., y(3) =c1y(1) + c2y(2)
  Time invariance:
    If two identical ﬁlters are used on two input sequences which are time-delayed versions of each other, then the observed output sequences will also be time-delayed versions of each other (with the same delay).

## Slide 6
An FIR ﬁlter modiﬁes the spectrum of an input sequence x, i.e, it changes the amounts (coeﬃcients) of the sinusoidal components of x. To illustrate this point, we take a single complex sinusoid of frequency ω:
  x[n]= ejωn ,n ∈ Z
  and put it through a ﬁlter with coeﬃcient vector b =[1 2 2 1]T .
  The output sequence y is given by
  y[n]= x[n]+2x[n − 1] + 2x[n − 2] + x[n − 3]
  = ejωn + 2ejω(n−1) + 2ejω(n−2) +ejω(n−3)
  = (1+2e−jω +2e-j2ω+e-j3ω) ejωn
  = (1+2e−jω +2e-j2ω +e−j3ω) · x[n]
Thus the output is a complex sinusoid of the same frequency; the ﬁlter merely scales the input by a complex factor which depends on the frequency ω. This is true for any FIR ﬁlter.

## Slide 7
The scaling factor above is known as the frequency response of the ﬁlter and is denoted by H(ejω):
H(ejω) = 1+2e−jω +2e-j2ω+e-j3ω
It is a polynomial in (negative) powers of ejω. The expression for H(ejω) can be simpliﬁed by noting the (non-circular) symmetry of the coeﬃcient vector
b = b0:3 = [1 2 2 1]T
about the “middle” index 3/2. Factoring out e−j3ω/2, we obtain
  H(ejω) = e−j3ω/2 (ej3ω/2 +2ejω/2 +2e-jω/2+e-j3ω/2)
  = e−j3ω/2 · (4 cos(ω/2) + 2cos(3ω/2))

## Slide 8
The modulus |H(ejω)| of the frequency response is known as the amplitude, or magnitude, response of the ﬁlter. In this case, noting that |ejθ| = 1, we have
|H(ejω)| = |4 cos(ω/2) + 2cos(3ω/2)|
This function of ω is symmetric about ω = π and has three zeros in the interval [0, 2π): at ω =2π/3, π and 4π/3. Thus for any of the three input sequences
x(1)[n]=ej2πn/3 , x(2)[n]=(−1)n, x(3)[n]=ej4πn/3 ,n ∈ Z,
the ﬁlter output equals 0 for all n. By linearity, the same is true about any linear combination of these three input sequences; in particular, the sequence x[n] = cos(2πn/3+φ0). Why?
This means that those frequencies have been filtered from the original input

## Slide 9
The angle ∠H(ejω) of the frequency response is known as the phase response of the ﬁlter. In this case, recalling that ∠z1z2 = ∠z1 + ∠z2, we have
∠H(ejω)= −(3ω/2) + ∠ (4 cos(ω/2) + 2cos(3ω/2))
The ﬁrst term is linear in ω, while the second equals 0 or ±π, depending on whether the real number 4 cos(ω/2) + 2cos(3ω/2) is positive or negative. This means that ∠H(ejω) is piecewise linear with constant slope (= −3/2) and discontinuities of size π occurring wherever 4 cos(ω/2) + 2cos(3ω/2) changes sign, i.e., at ω =2π/3, ω = π and ω =4π/3.
Note: The phase response ∠H(ejω) is piecewise linear for all FIR ﬁlters whose coeﬃcients have even or odd symmetry about the middle index (M/2).

## Slide 10
The expression for the frequency response H(ejω) is always periodic with period (in ω) equal to 2π; as a result, H(ejω) is (automatically) periodically extended outside the interval [0, 2π).
The amplitude response |H(ejω)| is symmetric (even) about ω = 0 and π, while the phase response ∠H(ejω) is antisymmetric (odd) about the same frequencies. This is true for all FIR ﬁlters with real-valued coeﬃcients b0,...,bM , since
H(e jω)= b0 + b1e-jω + ··· + bM e-jωM
and
H(e-jω)= H(ej(2π-ω))= b0 + b1ejω + ··· + bM ejωM = H∗(ejω)
(Recall that |z ∗| = |z| and ∠z* = −∠z.)

## Slide 11
Plotting |H(ejω)| and ∠H(ejω) requires computing H(ejω) at a suﬃciently dense set of frequencies ω in [0, 2π), i.e.,
ω = 0, 2π/N, 4π/N , . . . , 1 − 2π/N, where N >> M
These are the Fourier frequencies for a vector of length N. Provided N ≥ M +1, the resulting vector of values of H(ejω) equals the DFT of
[b ; 0N−M−1]

## Slide 12: Example
The following MATLAB script computes the amplitude and phase responses of the FIR ﬁlter with input-output relationship
  y[n]= x[n]+2x[n − 1] + 2x[n − 2] + x[n − 3]
  at N = 512 uniformly spaced frequencies in [0, 2π).
  b=[1 2 2 1].’ ;
  H = fft(b,512) ;
  A = abs(H) ; % amplitude response
  q = angle(H) ; %
  phase response
  w = (0: 1/512 : 1-1/512).’*(2*pi) ; plot(w,A) ; plot(w,q) ;

## Slide 13
Similar conclusions can be drawn when the input signal is a complex exponential, i.e.,
x[n]= zn, n ∈ Z
where z is an arbitrary complex number. Using the same ﬁlter as previously, we have, for all n,
    n−2 + z n−3
    y[n]= zn +2zn−1 + 2zn−2 + zn−3
    = (1+2z−1 +2z−2 + z−3) zn
    = (1+2z−1 +2z−2 + z−3) x[n]
The complex scaling factor
    H(z) = 1+2z−1 +2z−2 + z−3
is known as the system function of the ﬁlter. The frequency response H(ejω) of an FIR ﬁlter is the restriction of its system function to the unit circle z = ejω.

## Slide 14
Problems: 4.2, 4.4