## Slide 1: Lecture 5: Sampling of Continuous-Time Sinusoids Sections 1.6

## Slide 2: Key Points
Sampling a continuous-time sinusoid at a rate of fs =1/Ts (samples/second) produces a discrete-time sinusoid.
If the continuous-time sinusoid has angular frequency Ω = 2πf =2π/T , the resulting discrete-time sinusoid has angular frequency
ω =ΩTs =2πf/fs =2π Ts/T
At high sampling rates, discrete-time samples capture the variation of the continuous-time signal in great detail.
Two diﬀerent sampling rates fs =1/Ts and fs =1/Ts will produce samples having the same eﬀective frequency provided the sum Ts + Ts or the diﬀerence Ts - T s is an integer multiple of T =1/f

## Slide 3: The Sampling formula
The sampling formula
x[n]= x(nTs)
produces a sequence of samples x[n] from a continuous-time signal x(t). Ts is the sampling period and 1/Ts is the sampling rate. Applied to the continuous-time sinusoid
x(t) = cos(Ωt + φ),
this formula produces the discrete-time sinusoid
x[n] = cos(ΩTsn + φ)

## Slide 4: Example
The graph below shows a segment of the sinusoid
x(t) = cos((400π/3)t − π/8)
Your task: Using two types of stem lines, mark the samples in each of
x1[n] = cos((2π/5)n − π/8) (i.e., Ts =3.0 ms)
x2[n] = cos((2π/3)n − π/8) (i.e., Ts =5.0 ms)

## Slide 5: The Relationship Between Sampling rate and Sampling frequency
The frequency of the discrete-time sinusoid obtained by sampling is
ω =ΩTs =2πf/fs = 2πTs/T
Using this equation, it is easy to determine the relationship between sampling rate fs (samples/sec) to the frequency f (Hz) in order for the discrete-time sinusoid to be periodic.
Questions:
  What is this relationship?
  What is the equivalent condition in terms of Ts and T ?
  For what values of Ts is the discrete-time sequence x[n] constant in n?
  For what values of Ts is x[ · ] of the form . . . , a, −a, a, −a, . . .?

## Slide 6: Matlab Plot
Matlab only truly plots discrete signals
If the ratio Ts/T is small (i.e., fs/f is large), the sequence of samples x[n] closely tracks the variation in x(t). The smaller the ratio Ts/T , the easier it becomes to interpolate the discrete samples so as to approximate to the continuous-time signal.
This is how MATLAB produces a continuous plot.

## Slide 7: Effective Frequency Range
The range of values
Ts ∈ [0,T/2] or equivalently fs ∈ [2f, ∞]
corresponds to ω ∈ [0,π], which is the eﬀective frequency range for real sinusoids.
If Ts > T/2, or equivalently, if fs < 2f, the sequence of samples obtained from x(t) has the same frequency as one obtained using a smaller sampling period (or higher sampling rate).
There are inﬁnitely many sampling rates that produce eﬀectively the same ω in x[n].
Recall that ω and ω can be used to describe the same discrete-time sinusoid provided
ω = ±ω +2kπ
for some integer k. Thus if fs and f are two sampling rates such that
f/fs ± f/fs = k
or equivalently, if
Ts ± T’s = kT ,
then the two resulting sample sequences will have the same (angular) frequency, provided that frequency is expressed in the interval [0,π].

## Slide 8: Example
Consider the continuous-time sinusoid
x(t) = cos((400π/3)t − π/8)
and the discrete-time sinusoids
x1[n] = cos((2π/5)n − π/8)
x3[n] = cos((2π/5)n + π/8)
Here T = 15.0 ms, f = 200/3 Hz.

## Slide 9: Example
The smallest Ts which produces x1[ · ] equals (from ω =ΩTs)
Ts = (2π/5) (3/400π) = 3.0ms
The remaining values of Ts which produce x1[ · ] are given by
Ts =3.0+ k(15.0) ms, k =1, 2,...
As for x3[ · ], we use cos(−θ) = cos(θ) to express it as
x3[n] = cos(−(2π/5)n − π/8)
The values of Ts which produce x3[ · ] are thus
Ts = −3.0+ k(15.0) ms, k =0, 1,...
Since Ts is necessarily positive, it follows that
Ts = 12.0+ k(15.0) ms, k =1, 2,...