## Slide 1: Lecture 17: Response of FIR filters to exponential inputs, response of FIR filters to periodic inputs, cascaded filters Sections 4.4.2,4.4.4, 4.4.5 Sections 2.2.3, 2.3

## Slide 2
We have seen that if x[n]= zn is the input to an FIR ﬁlter with coeﬃcients b0,...,bM , then the output y[ · ] is given by y[n]= H(z), where
H(z)= b0 + b1z−1 + ··· + bMz−M
is the ﬁlter’s system function.

## Slide 3
If the input is the real-valued sinusoid
x[n] = cos(ω0n + φ)= (1/2)ejφejω0n+(1/2)e-jφe-jω0n ,
then, by linearity, the output is given by
y[n]= (1/2)H(ejω0 )ejφejω0n + (1/2)H(e −jω0 )e−jφe−jω0n
Since H(e-jω), = H∗(ejω), the expression above equals the sum of two complex conjugate terms, which is the same as twice the real part of either term:
y[n]= Re{H(ejω0 )ej(ω0n+φ) )

## Slide 4
Writing H(ejω0 ) in complex exponential form, i.e., H(ejω)= |H(ejω)| ej∠H(ejω), we obtain
y[n]= |H(ejω0 )|cos (ω0n + φ + ∠H(ejω0)) (n ∈ Z)
The same approach can be applied to the oscillating exponential input
x[n]= rn cos(ω0n + φ)= ((ejφ)/2) rn ejω0n+ ((e-jφ)/2) rn e-jω0n
Taking z = re±jω0 , we obtain in this case
y[n]= |H(rejω0 )| rn cos (ω0n + φ + ∠H(rejω0)) (n ∈ Z)

## Slide 5
Example:
  Let x[n]=2-n · cos (πn/3 + π/4), n ∈ Z
  and y[n]= x[n] + 2x[n − 1] + 2x[n − 2] + x[n − 3]
  Setting z =(ejπ/3)/2, we obtain
    H(z) = 1+4e−j(π/3) +8e−j(2π/3) +8e−jπ = 13.748 e−j2.285
  The output sequence is therefore given by
    y[n] = 13.748 · 2−n · cos(πn/3 − 1.499) ,n ∈ Z
  Your task: Repeat for x[n] = cos(πn/3+ π/4).

## Slide 6
Periodic sequences are always expressible as sums of sinusoids. We have seen that if x[ · ] is periodic with period L, then it can be written as
where X [0 : L − 1] is the DFT of its ﬁrst period x[0 : L − 1]. Thus x[ · ] is a linear combination of L (or fewer) complex sinusoids, whose frequencies are multiples of 2π/L.

## Slide 7
Example:
Suppose
  x[n]= A1 cos(2πf1n + φ1)+ A2 cos(2πf2n + φ2)+ A3 cos(2πf3n + φ3) ,
  where the Ai’s are real and nonzero, and
    f1 = 1/8, f2 =3/20, and f3 = 5/12;
Each fi is rational, therefore each sinusoid is periodic. Their sum x[ · ] is also periodic, and its period is the smallest value of L for which all three frequencies are multiples of 1/L. Thus L equals the least common multiple of 8, 20 and 12, namely L = 120. Obviously, the spectrum of x[ · ] has only six (out of 120 possible) lines in [0, 2π).
Note: In discrete time, the sum of two or more periodic signals is always periodic. This is not true in continuous time.

## Slide 8
If the periodic signal x[ · ] from above is the input to an FIR ﬁlter with frequency response H(ejω), then, by linearity, the ﬁlter output is given by
Thus the output sequence y[ · ] is also periodic with period L, and its ﬁrst period y[0 : L − 1] has DFT Y[0 : L − 1] given by
(♠)

## Slide 9
As we saw earlier, H(e−jωn ) = bne−jωn (for n = 0 to M) can be computed for any set of M + 1 or more uniformly spaced frequencies by zero-padding the vector b and computing a DFT. Thus (♠) suggests a way of computing the response of an FIR ﬁlter to a periodic input of period L (where L ≥ M + 1) using a frequency domain-based tool, namely the element-wise multiplication of two DFT’s.

## Slide 10
Example:
Consider the ﬁlter with input-output relationship
  y[n]= x[n] − 4x[n − 1] + x[n − 2]
Suppose that the input x[ · ] is periodic with period L = 4, such that x[0:3] = [2 1 −3 5]T
The MATLAB script below computes the ﬁrst period y[0 : 3] of the output.
x=[2 1-3 5].’;
X = fft(x) ;
b=[1-4 1].’;
H = fft(b,4) ;
Y = H.*X ; y = ifft(Y)

## Slide 11
Since element-wise multiplication of DFT’s is equivalent to circular convolution in the time domain, (♠) suggests that the response of an FIR ﬁlter to a periodic input can be computed using a circular convolution in the time domain. This is not surprising: by rewriting the input-equation
y[n]= x[n] − 4x[n − 1] + x[n − 2]
in the previous example as
y[n]= x[n] − 4x[n − 1] + x[n − 2] + 0 · x[n − 3] ,
we obtain
This is the circular convolution of x[0 : 3] and [b; 0], which is precisely what the MATLAB script (above) computes.

## Slide 12
If two FIR ﬁlters are connected in series, or in a cascade (as shown below), the resulting system function is given by the product of the two system functions, i.e.,
H(z)= H1(z)H2(z)
(Note that the order in which the two ﬁlters are connected is immaterial.) This is proved by using x[n]= zn as the input to the cascade. The output of the ﬁrst ﬁlter is
y(1)[n]= H1(z)zn, (n ∈ Z)
and, by linearity, the output of the second ﬁlter (same as the output of the cascade) is
y(2)[n]= y[n]= H1(z)H2(z)zn = H2(z)H1(z)zn (n ∈ Z)
H1
H2
x = x(1)
y(1) = x(2)
y(2) = y

## Slide 13: Example
Two FIR ﬁlters with coeﬃcient vectors
b(1) = [1 2 2 1]T
b(2) = [1 -4 1]T
are connected in cascade. The resulting ﬁlter has system function H(z) = (1+2z −1 +2z −2 + z −3)(1 − 4z −1 + z −2)
=1 − 2z−1 − 5z−2 − 5z−3 − 2z−4 + z−5
and is therefore an FIR ﬁlter with coeﬃcient vector
b = [1 −2 −5 −5 −2 1]T
and input-output relationship
y[n]= x[n] − 2x[n − 1] − 5x[n − 2] − 5x[n − 3] − 2x[n − 4] + x[n − 5]

## Slide 14
Problems: 4.5, 4.7, 4.8,