## Slide 1: Lecture 12: Introduction to Discrete Fourier Transform Sections 2.2.3, 2.3

## Slide 2: The discrete Fourier transform (DFT) is a powerful computational tool. It allows us to resolve ﬁnite-dimensional signal vectors into sinusoids of diﬀerent frequencies, some of which may be more prominent than others. For example, the 200-point signal vector s constructed in n = (0:199).’; s = 4.7*cos(0.12*pi*n-1.3) + ... 3.8*cos(0.19*pi*n+0.8) + ... 5.1*cos(0.23*pi*n+2.4) + ... 2.0*randn(size(n)); plot(n,s) is the sum of three real-valued sinusoids plus noise. This is not at all that obvious from a plot of the signal. If, however, we compute S = fft(s); bar(abs(S)) then we obtain a symmetric graph with three clear peaks on either half. These peaks corre­spond to the main frequency components at ω = (0.12)π, (0.19)π and (0.23)π. Based on this information, we can characterize the signal s as a sum of three sinusoids plus noise.

## Slide 3: The MATLAB command FFT computes the DFT S of a signal vector s. S is a complex-valued vector of the same size as s, whose entries reﬂect the relative amounts of the sinusoidal components of s. The number of frequencies involved is the same as the size of s, and as we will soon see, these frequencies are uniformly spaced in [0, 2π). The principle behind the DFT is already familiar to us: a vector s of size N is expressed as a linear combination of the columns of a N × N matrix V, i.e., s = Vc Each column of V is a complex-valued sinusoid, i.e., it is given by the formula ejωn, where n is the row index representing time. No two columns use the same frequency ω; moreover, the N frequencies are chosen such that the columns of V are orthogonal: VH V = diagonal matrix This simpliﬁes the computation of the coeﬃcients c, since (VH V)c = VH s reduces to a diagonal system of equations. (The DFT S is deﬁned simply as Nc.)

## Slide 4: We have already encountered the matrix V in the case N = 4: V =[v(0) v(1) v(2) v(3)] = Each column (from left to right) is a complex-valued sinusoid of frequency ω =0, π/2,π and 3π/2 Note that the four frequencies are uniformly spaced over [0, 2π) (or the unit circle).

## Slide 5: In the general case (i.e., for arbitrary N), the frequencies of the N sinusoids are also uniformly spaced over [0, 2π). Speciﬁcally, the kth column of V (starting with k = 0) is a complex-valued sinusoid of frequency ω = 2π k /N This choice of ω makes the sinusoid ejωn periodic with period equal to N or a submultiple thereof. No other values of ω result in this property. If we set v = ej(2π/N), then the columns of V are formed by raising the complex constants v0 =1, v, v2, ..., vN-1 to powers n =0: N − 1. These N complex numbers are precisely the roots of zN = 1.

## Slide 6: The orthogonality of the columns of V can be shown using the geometric sum formula If v(k) and v(l) are two diﬀerent columns of V, (since v(l−k)N = 1). On the other hand, This establishes the general result VH V = NI

## Slide 7: In the case N = 6, the Fourier frequencies are ω =0, π/3, 2π/3 ,π, 4π/3, 5π/3 and the columns of V are sinusoids at these frequencies: In this case, v = ej(2π/6) = ejπ/3) and vnk = vnk = ej(π/3) nk If s =[1 2 3 6 5 4]T , then the coeﬃcients c in s = Vc are quickly found using c = fft([1 2 3 6 5 4].’)/6 By hand, we have ck = <v(k), s>/6. Thus for example (note the complex conjugation!), c0 = (1+2+3+4+5+6)= 7/2 c1 = 1+(1 − j3)+ (−1 − j3) − 6+ (5/2)(−1+ j3) + 2(1 + j3)= −1+ j3/3 c5 = 1+(1+ j3)+ (3/2)(−1+ j3) − 6+(5/2) (−1 − j3) + 2(1 − j3)= −1 − j 3/3
EXAMPLE

## Slide 8: An alternative—and equivalent—notation for the projection of s onto the columns of V involves the discrete Fourier transform S, deﬁned by S = VH s This vector consists of the N inner products <v(k), s>, where k =0: N − 1. Since the index k represents frequency (the frequency ωk = k(2π/N)), the DFT vector S is a signal in the so-called frequency domain. It is also known as the spectrum of s.

## Slide 9: The projection coeﬃcients (in the previous notation) are given by c = (1/N)VH s =(1/N) S Thus s = Vc = (1/N)VS The signal s is also referred to as the inverse DFT of its spectrum S. The matrix V is symmetric, since Vnk = ej(2π/N)kn = Vkn. Therefore by definition: VH = V∗ = W

## Slide 10: To understand the meaning of the DFT (or spectrum), suppose Both s and S are of size N = 8. Since S has only one nonzero entry, s can be formed using one column of V only, namely the k = 0th column (= v(0)). This means that s consists of a single sinusoidal component at frequency ω =0 · (2π/8) = 0; that sinusoid is, of course, constant in time. Thus s is a constant vector, and its value can be found from the synthesis equation: s = (1/8)VS = (1/8)v(0) Your task: Verify this result using the IFFT command in MATLAB.
EXAMPLE

## Slide 11: Like any DFT pair, the pair s ←→ S in the above example can be also obtained in the reverse direction, i.e., starting from and using the analysis equation S = VH s The right-hand side computes the inner product of each column of V with s. Since s is a scaling of the zeroth column of V, and since the columns of V are orthogonal, the result is Your task: Verify this calculation using the FFT command in MATLAB. This example can be generalized to any DFT that has a single nonzero entry.

## Slide 12: 1)The least-squares approximation of any real or complex-values signal s based on any subset of the N complex Fourier sinusoids is given by the sum of the projections of s onto each of the sinusoid; the projection of s onto v(k), is given by: ck v(k), where ck = <v(k), s>/N 2) The least-squares approximation of s based on all N complex Fourier sinusoids is an exact representation of s and is given by s = Vc
Signal Representation

## Slide 13: . Problems: 3.2, 3.4