# MONTGOMERY COLLEGE, ROCKVILLE

# Physics, Engineering and Geosciences Department

# EE 244 – Digital Logic Design

Practice Midterm

- (3) convert the following unsigned integer to decimal: 110011001100

- (3) Convert the following decimal number to hexadecimal: 791

- (4) The following decimal integers are to be stored in a 6-bit two’s complement format. Show how they are stored.   a. +32  b. -32  c. -16

- (7) In IEEE standard 32-bit notation, how would the following decimal be stored?  -48.5

- (8) Reduce the expression to a minimum SOP form, using P1 through P12.

h = ab’ + bc’d’ + abc’d + bc (3 terms, 5 literals)

- (25) For the following circuit:

  - Compute the maximum delay,

    - Assuming that all inputs are available both uncomplemented and complemented

    - Assuming only uncomplemented inputs are available, and an additional gate must be added to complement each input

  - Compute the maximum delay from input D to the output, assuming only uncomplemented inputs are available, and an additional gate must be added to complement each input

- (25) Design a priority encoder with seven active low inputs, p1, . . . , p7 and three active high outputs, CBA that indicate which is the highest priority line active is designed using AND, OR, and NOT gates. Input p1 is highest priority; p7 is lowest. If none of the inputs are active, the output is 000. Assume that is a fourth output line, M, which is 1 if there are multiple active inputs. Show the truth table and Boolean expressions for C, B and A.

- (25) Design a 2-bit comparator that compares two 2-but numbers A and B (A1A0 and B1B0) with the following outputs:

  - X:A>B,

  - Y: A=B

  - Z: A<B

Show the truth table, kaurnaugh maps and minimum SOP expression for each output. Also minimize the expression using XOR or XNOR gates where necessary.