## Slide 1: Lecture 4: Phasors; Discrete-Time Sinusoids Sections 1.4, 1.5

## Slide 2: Key Points
The stationary phasor of Acos(t + ) is the complex number Aej. The sum of two (or more) sinusoids of arbitrary amplitudes and phases but of identical frequency  is a sinusoid of frequency . Sinusoids of identical frequency can be added together by taking the complex sum of their stationary phasors.
The discrete time parameter n counts samples. The (angular) frequency parameter  is an angle increment (radians/sample). Physical time (seconds) is nowhere involved.
Frequencies  and  + 2 are equivalent (i.e., produce the same signal) for real or complex sinusoids in discrete time.
Frequencies  and 2 -  can be used alternatively to describe a real sinusoid in discrete time:
cos( n + ) = cos(-  n - ) = cos((2- )n - )
The effective range of frequencies for a real sinusoid in discrete time is 0 (lowest) to  (highest).
A discrete-time sinusoid is periodic if and only if  is of the form
 =(2k/N)
for integers k and N. The fundamental period is the smallest value of N for which the above holds.

## Slide 3: Stationary Phasor
Since cos θ = Re{ejθ}, it follows that x(t) is the real part of the time-dependent complex sinusoid
z(t) = Aej(t+)
On the complex plane, the point z(t) moves with constant angular velocity  on a circle of radius A. Its projection on the real axis equals x(t). The initial position
z(0) = Aej ,
viewed as a vector, is known as the stationary phasor of x(t).

## Slide 4: Addition of two sinusoids
Two real-valued sinusoids of the same frequency can be added together:
A1cos(Ωt + φ1)+ A2 cos(Ωt + φ2)= Re{A1ej(Ωt+φ1) + A2ej(Ωt+φ2)}
= Re{(A1ejφ1 + A2ejφ2 )ejΩt}
= A cos(Ωt + φ)
where
Aejφ = A1ejφ1 + A2ejφ2
The result is a sinusoid of the same frequency, whose stationary phasor is the complex (i.e., vector) sum of two component stationary phasors.

## Slide 5: Example
2.7 cos(15πt +0.6) + 4.1 sin(15πt − 1.8) = A cos(15πt + φ)
where
Aejφ =2.7ej0.6 +4.1ej (−1.8−π/2)
We convert each term to its Cartesian form, compute the sum and convert back to polar form to obtain A =3.0241 and φ =2.1937.
Your task: Fill in the missing steps.

## Slide 6: Discrete-Time Signals
A discrete-time signal is a sequence of values (samples) x[n], where n ranges over all integers. A discrete-time sinusoid has the general form
x[n]= A cos(ωn + φ)
or, in its complex version,
z[n]= Aej(ωn+φ)
Question: How is x[n] related to z[n]?

## Slide 7: Matlab Example
Use MATLAB to generate 100 values of each of the discrete-time sinusoids x1[n] and x2[n]:
  n = 0:99;
  w1 = pi/25; q1 = 2*pi/5;
  x1 = cos(w1*n + q1);
  w2 = 2.4; q2 = -1.3;
  x2 = cos(w2*n + q2);
  bar(n,x1) % discrete bar graph
  plot(n,x1), grid % extrapolated graph
  bar(n,x2) % no resemblance to a continuous-time sinusoid
Depending on its frequency, a discrete-time sinusoid may look similar to, or quite diﬀerent from, a continuous-time one.

## Slide 8: Frequency of a Discrete-Time Sinusoid
The frequency parameter ω is measured in radians, or radians per sample. (Unlike Ω, which is in radians per second). Thus the frequency of a discrete-time sinusoid is just an angle increment: the argument of cos(·) increases by a ﬁxed amount ω with each sample.
Two key observations:
  ω and ω +2kπ, where k is an integer, represent the same frequency. This is because ωn and (ω +2kπ)n diﬀer by 2knπ radians, i.e., a whole number of revolutions, and therefore at every time n,
  cos(ωn + φ) = cos((ω +2kπ)n + φ)
  ej(ωn+φ) = ej((ω+2kπ)n+φ)
  Typically, the range of ω is chosen as [0, 2π) or (−π, π].
  In the real-valued case, either ω or −ω can be used to express the same sinusoid. This is due to the identity cos θ = cos(−θ), which implies that for every n,
  cos(ωn + φ) = cos(−ωn − φ)
  As a result, the range of ω for real-valued sinusoids can be limited to [0,π].

## Slide 9: Frequency of a Discrete-Time Sinusoid

## Slide 10: Classwork
Find simple expressions for x[n]= A cos(ωn + φ) when ω = 0 (lowest possible frequency) and ω = π (highest possible frequency).
Modify the MATLAB script given earlier to compute and plot 100 values of the high-frequency sinusoid
x3[n] = cos((24π/25)n +2π/5)
Note that the frequencies of x1[n] and x3[n] are complementary to each other in the interval [0,π].

## Slide 11: Fundamental Period
The fundamental period of x[n] is the smallest integer N such that
(∀n) x[n + N]= x[n]
If no such N exists, then the signal is nonperiodic (or aperiodic).
The sequences cos(ωn + φ) and ej(ωn+φ) are repetitions of a ﬁxed vector of N values if and only if the argument ωn + φ changes by an exact multiple of 2π every N time indices. In other words, if and only if
ωN =2kπ ⇔ ω = ·2πk/N
for some integer k.
The smallest value of N satisfying the above relationship is the fundamental period.

## Slide 12: Example
Shown is the fundamental period N (where periodic).
ω =0 ⇒ N =1 ω = π ⇒ N =2
ω =1.0 ⇒ N = ∞ (i.e., nonperiodic)
ω = 10π/13 ⇒ N = 13
ω = 11π/13 ⇒ N = 26
Note that for a periodic discrete-time sinusoid, the fundamental period does not necessarily equal 2π/ω (as was the case with continuous-time sinusoids).